## Slide 1: NextCare: An Intelligent System for the Low-Cost Early Diagnosis and Real-Time Monitoring of Parkinson’s Disease using Machine Learning, Signal Processing and Wearable Technology
By Shreyas Kar

## Slide 2: Purpose: Issues with PD Diagnosis
Late Diagnosis
Inaccurate Diagnosis

## Slide 3: Purpose: Issues with PD Monitoring
Lack of Monitoring
Shortage of Neurologists

## Slide 4: NextCare
3D printed Wearable Device + App
Algorithms for
  Early Diagnosis by voice.
  Continuous monitoring of tremor.

## Slide 5
NextCare
Diagnosis
Voice Pattern
Monitoring
Tremor

## Slide 6: Voice Biomarker
Voice is first markers of Parkinson’s Disease
Change in voice pattern is not apparent
Machine Learning
Signal Processing
Approach
Diagnosis

## Slide 7
Voice Sample
Voice Attributes
(50)
Features
(2)
Signal Processing
PCA + Heat Map
Shimmer, Jitter, RPDE,
PPE, Spread etc.
PPE, Spread1
Feature Computation
Data
Diagnosis

## Slide 8: Model Training and Testing
F2 = 0.94
F2 = 0.93
F2 = 0.93
Artificial Neural Network (ANN)
Logistic Regression
Support Vector Machine (SVM)
Success Criterion: 0.87 F2 score
Diagnosis
Data

## Slide 9: Demo - NextCare Diagnosis
Diagnosis

## Slide 10: NextCare Monitoring System
IMU
/Inertial Sensors
Bluetooth
UPDRS
Tremor Amplitude
and Constancy
NextCare App
Cloud Database
Algorithm
Algorithm
NextCare App
Monitoring
UPDRS *Chart
Real Time Tremor Visualization

## Slide 11: Parkinsonian Tremor Quantification by Amplitude and Frequency
Tremor Score
Amplitude
Normalized Peak Power Sum of all axes in IMU sensor.
Constancy
Tremor score computed every 15 min for a span of week.
Data
Monitoring

## Slide 12
Chart: Neurologist vs Predicted – Constancy of Rest Tremor
| 0s | 1s | 2s | 3s | 4s
Neurologist | 9 | 3 | 5 | 6 | 11
Algorithm | 7 | 5 | 6 | 5 | 11
Chart: Neurologist Vs Algorithm - Rest Tremor Amplitude
| 0s | 1s | 2s | 3s | 4s
Neurologist | 41 | 15 | 9 | 3 | 0
Algorithm | 39 | 17 | 9 | 3 | 0
Accuracy: 94.1%
Accuracy: 91.1%
Data
NextCare Monitoring Results
Monitoring

## Slide 13
Indicative of Treatment Failure
If NextCare not there and patient is treated on a bad day (2/6/21)
NextCare Monitoring Use Cases
Monitoring

## Slide 14: Wearable Device Construction
Constructed using Google SketchUp Software and Ender 3 Pro 3D Printer , PLA Filament

## Slide 15: Demo - NextCare Monitoring
Monitoring

## Slide 16: NextCare Mobile App
Registration
Login
Home
Diagnosis
Home
PD Diagnosis
Voice
Collection
Connect
Device
Monitoring
Tremor
A few Screens

## Slide 17: Conclusion: NextCare at a Healthcare Setting
NextWatch on a patient
NextCare receiver app on phone or Laptop
Google Cloud Firestore Database
Doctor checks real-time report on NextCare App
Patient’s 30s voice sample collected by NextCare App
Doctor checks result on NextCare App
Diagnosis
Monitoring
Diagnosis 5 years before existing methods.
19% better accuracy than existing methods.

## Slide 18: Acknowledgment
Dr. Peter Campbell: Researcher University of Louisville Department of Anatomical Sciences and Neurobiology
Dr. Joseph Neimat: Chairman of Department of Neurological Surgery at the University of Louisville
Michael. J. Fox Foundation: Funding clinical trials that provided the data for training and testing models.

## Slide 19: Next Step
Add Bradykinesia and Gait to monitoring.

## Slide 20: Thank you!

## Slide 21
Appendix

## Slide 22: Works Cited
Ahire, J. B. (2018, August 29). The Artificial Neural Networks handbook: Part 1. Retrieved from https://medium.com/coinmonks/the-artificial-neural-networks-handbook-part-1-f9ceb0e376b4.
Bhandari, S. (2019, June 19). Dopamine: What It Is & What It Does. Retrieved from https://www.webmd.com/mental-health/what-is-dopamine#1.
Brid, R. S. (2018, September 28). Linear Regression: Is a Line Reasonable ? Retrieved from https://medium.com/greyatom/linear-regression-is-a-line-reasonable-b1c8f94d03d7.
'Exploiting Nonlinear Recurrence and Fractal Scaling Properties for Voice Disorder Detection', Little MA, McSharry PE, Roberts SJ, Costello DAE, Moroz IM. BioMedical Engineering OnLine 2007, 6:23 (26 June 2007)
F 0.5 and F2 Scores. (2016, June 13). Retrieved from https://www.litigationsupporttipofthenight.com/single-post/2016/06/13/F-05-and-F2-Scores.
How Parkinson's Disease Is Diagnosed. (n.d.). Retrieved from https://www.hopkinsmedicine.org/health/treatment-tests-and-therapies/how-parkinson-disease-is-diagnosed.

## Slide 23: Works Cited Continued
Mayfield Brain & Spine. (n.d.). Parkinson's Disease (PD). Retrieved from https://mayfieldclinic.com/pe-pd.htm.
Online Courses From Top Universities. Join for Free. (n.d.). Retrieved from https://www.coursera.org/learn/machine-learning/home/welcome.
Parkinson's disease. (2018, June 30). Retrieved from https://www.mayoclinic.org/diseases-conditions/parkinsons-disease/symptoms-causes/syc-203760
Ray, S., & Business Analytics and Intelligence. (2019, September 4). 7 Regression Types and Techniques in Data Science. Retrieved from https://www.analyticsvidhya.com/blog/2015/08/comprehensive-guide-regression/.
Schwab, P., & Karlen, W. (2019). PhoneMD: Learning to Diagnose Parkinson’s Disease from Smartphone Data. Proceedings of the AAAI Conference on Artificial Intelligence, 33, 1118–1125. doi: 10.1609/aaai.v33i01.33011118
Tsoulos, I. G., Mitsi, G., Stavrakoudis, A., & Papapetropoulos, S. (2019). Application of Machine Learning in a Parkinsons Disease Digital Biomarker Dataset Using Neural Network Construction (NNC) Methodology Discriminates Patient Motor Status. Frontiers in ICT, 6. doi: 10.3389/fict.2019.00010
Tucker, C., Han, Y., Nembhard, H. B., Lee, W.-C., Lewis, M., Sterling, N., & Huang, X. (2015). A data mining methodology for predicting early stage Parkinsons disease using non-invasive, high-dimensional gait sensor data. IIE Transactions on Healthcare Systems Engineering, 5(4), 238–254. doi: 10.1080/19488300.2015.1095256
What Is Parkinson's?: Parkinson's Foundation. (n.d.). Retrieved from https://www.parkinson.org/understanding-parkinsons/what-is-parkinsons.
Zhang, K., & Demner-Fushman, D. (2017, July 1). Automated classification of eligibility criteria in clinical trials to facilitate patient-trial matching for specific patient populations. Retrieved from https://www.ncbi.nlm.nih.gov/pmc/articles/PMC6080677/

## Slide 24: QALYs gain - Early Detection of PD

## Slide 25: Overall Process Flow Diagnosis System
PD
Diagnosis
Computes Voice
Features
Algorithm
ML Algorithm
NextCare App
Diagnosis

## Slide 26
Real-time Visualization of Tremor (Sensor Data)
Data
Monitoring

## Slide 27: Quantification of UPDRS
Tremor Amplitude Constancy Tremor
Monitoring

## Slide 28: Features for ML Algorithms
1. Pitch Period Entropy
2. Spread1
Voice Sample
Conversion
Pitch Sequence
39.87*log(Fundamental Frequency
/50)
Semitone Scale
Entropy of Probability Distribution
PPE
Diagnosis

## Slide 29: Privacy
Created an authentication mechanism so only neurologist and patient can view data
All personally identifiable data encrypted before entering the database.

## Slide 30: Comparison to Existing Methods
Most Intelligent Systems for Parkinson’s only perform monitoring
My system provides for early diagnosis of PD
First system to use UPDRS scale for monitoring, exactly replicating what a neurologist would see.

## Slide 31: Limitations
Tradeoff between invasiveness and performance
Collecting more features would slightly increase performance